## Slide 1: The ALLEGRO design and safety studies
CATHARE Gas Seminar
Saclay, 25-26 January 2018
A. Vasile
CEA
V4G4 Centre of Excellence – ALLEGRO Project

## Slide 2
Very High Temperature Reactor
Sodium Fast Reactor
Super Critical Water Reactor
Molten Salt Reactor
Lead Fast Reactor
Gas Fast Reactor
GIF Selection of six Nuclear Systems
Recognition of the major potential of fast neutron systems with a closed fuel cycle for breeding (fissile re-generation) and waste minimization (minor actinide burning)

## Slide 3
MYRRHA
Flexible Irradiation Facility
ASTRID
SFR
Prototype
ALLEGRO
GFR
Experimental reactor
75 MWth
Helium
MOX/UOX, then UPuC
100 MWth
Lead-Bismuth
MOX
300 MWth / 120 MWe
Lead
MOX
ALFRED
LFR Demonstrator
1500 MWth / 600 MWe
Sodium
MOX
R&D on Fast Reactors in Europe
ESNII
Reactors under development

## Slide 4
GFR and ALLEGRO
Allegro 75 MWt
V4G4 Centre of Excellence
Hungary, Czech Republic, Slovakia and Poland
From 2017: CEA Associated Member
Euratom countries
GFR 2400 MWt
reference concept

## Slide 5
Objectives of ALLEGRO
  Demonstration of key GFR technologies:
      Development of ceramic fuels
      Helium circuits and components
      Decay heat removal
  Fast neutron irradiation capacity
  Potential for coupling with high temperature components or direct use of heat
  Development of safety standards for GFRs

## Slide 6
  75 MWth nominal power
  Primary He (260-530°C core inlet-outlet, 70 bars)
  2 Secondary pressurized water loops, option for an additional high temperature gas loop.
  Tertiary athmospheric air (No power conversion)
  3 DHR loops (Primary He / Water HX)
IHX He/water
DHRS
RPV
Additional He/He IHX
Main blowers
Guard containment
ALLEGRO Main characteristics

## Slide 7
DHR Blower
DHR HX
DHR Valve
Primary Blower
Primary
Valve
Water Pump
Pressurizer
Aero
Core
530 °C
260 °C
70 b
197 °C
127 °C
65 b
He
Water
75 MWth
Water pool
DHR circuits
(1/3)
Primary circuits
(1/2)
Secondary circuits
(1/2)
He
Pony motor
Nitrogen accumulators (1/3)
Guard vessel
Air Blower
10 b
65 b
ALLEGRO Main characteristics

## Slide 8
Acceptance criteria
Selection of transients
Core/System feasibility studies
CATHARE
RELAP
MELCOR
Detailed MOX core neutronic,
thermalhydraulic,
mecanic,
fuel behaviour calculations and optimization
UOX core neutronic feasibility study
Detailed UOX core neutronic,
thermalhydraulic,
mecanic,
fuel behaviour calculations and optimization
Initial reference core and systems design
S-ALLEGRO
Loop
Trnava
Loop
Code to code thermal hydraulic benchmark
(VINCO EU project)
Code to code neutronic benchmark
(VINCO EU project)
Yes
No
ALLEGRO CORE an systems feasibility studies

## Slide 9
VINCO Thermal Hydraulic Benchmark
 | Case 1 | Case 2
Initial conditions | Nominal | Nominal
Transient | LOCA 3' breach in primary cold leg. | SBO Total loss of electricity.
 | MTA EK (HU) | NCBJ (PL) | UJV (CZ) | VUJE (SK)
CATHARE 2 |  |  |  | 
RELAP 3D |  |  |  | 
MELCOR 2.1 |  |  |  | 
Codes used
Calculated transients

## Slide 10: He-loop S-ALLEGRO (CZ)
ALLEGRO mockup
Phase I (SUSEN 2017)

## Slide 11: STU-loop Trnava (SK): External view

## Slide 12
Class 4
10-4/y - 10-7/y
Hypothetical accidents
Plant restart not required
850 °C
DEC
Design Extension Conditions
1300 °C
CATHARE calculations of protected transients on the reference 75 MW design. Transients |  | Additional failures |  |  |  |  |  |  |  | 
 |  | None | 1 Pony motor off | Secondary pumps off | Tertiary blowers off | 1 DHR loop valve | 1 primary valve | 1 DHR loop | 1 DHR blower | Guard vessel
Pressurized | LOFA Primary |  |  |  |  |  |  |  |  | 
 | LOHS |  |  |  |  |  |  |  |  | 
 | Internal breach |  |  |  |  |  |  |  |  | 
 | SBO |  |  |  |  |  |  |  |  | 
 | Water ingress in the core |  |  |  |  |  |  |  |  | 
LOCA | Primary 3' |  |  |  |  |  |  |  |  | 
 | Primary 10' |  |  |  |  |  |  |  |  | 
 | Secondary 10' |  |  |  |  |  |  |  |  | 
 | DHR loop 10' |  |  |  |  |  |  |  |  | 
 | Crossduct rupture |  |  |  |  |  |  |  |  | 
 | Total section break colduct |  |  |  |  |  |  |  |  | 
 | Primary 1' + SBO |  |  |  |  |  |  |  |  | 
Class 3
10-2/y - 10-4/y
Accidents
Plant restart required
735 °C
Safety classes and criteria for maximum
SS cladding temperatures
 Criteria satisfied
 Criteria not satisfied

## Slide 13
      Core design
    Decrease total power (Reference: 75 MW)
    Decrease power density (Reference 100 MW/m3)
    Increase thermal inertia (Reflectors…)
    Decrease pressure drop to enhance natural convection
    Cladding material for the start-up oxide core (Reference SS)
      Optimization of DHR Systems
    Coupled primary-secondary turbomachines
    Injection systems, Heavy gas accumulators
      Guard containment
    Guard containment + Conventional containment building as back-up
    Optimization of guard containment to assure the required back-up pressure to maintain an efficient cooling by natural convection.
    Provisions to assure that a double failure (primary circuit and guard containment) is impossible or very unlikely
CATHARE, RELAP an MELCOR system codes are being used for system analysis
Improvement of DHR capabilities in case of LOCA+SBO

## Slide 14
1 inch LOCA + BLACKOUT Effect of power and power density reduction on the maximal peak cladding temperature
Chart: Time [s]
CATHARE calculations

## Slide 15
Improvement of DHR capabilities in case of LOCA+SBO
      First core of ALLEGRO must:
        Rely on already existing technologies.
        Be used for the development of advanced GFR ceramic fuel by irradiation on some dedicated positions.
      MOX fuel was considered in previous stages of the project. "CEA2009" MOX core main characteristics:
        75 MW
        100 MW/m3
        1 batch, 660 fped
        25 % Pu
        Carbide experimental S/As:
          8,4 1014 n/cm2/s max fast flux (GFR2400 – 30%)
          1,8 at% max burn up (GFR2400 – 10%)
          15 dpa SiC max dose (GFR2400 – 32%)
      Design options for make a LEU UOX core feasible
        Increase the number of fuel assemblies
        Increase the core hight
        Increase to pin diameter.
Experimental
MOX
Control
Shutdown

## Slide 16
      The ALLEGRO Design and Safety Roadmap was defined and is being implemented by the V4G4 partners.
      Benchmarking VINCO activities by comparing thermalhydraulic system codes are being performed in support of the improvement of the design.
      ALLEGRO design is being improved to increase the decay heat removal capabilities in case of a very unlikely transient of loss of coolant accident cumulated with a total station blackout.
      Feasibility of a UOX stat-up core is being investigated
SUMMARY